## Slide 1: UPH Simulation with Automation Line Layout.

## Slide 2: Objectives
Validate a line configuration faster and accurate.
Reduce experiments in a physical line by validating a concept before implementation.

## Slide 3: Requirements
Allow user to define number of stations in a assembly line.
Allow user to define number of zones per station.
Allow user to define a cycle time of each zone.
Allow user to define zone-to-zone transfer time of each station.
Allow user to define unload-zone to load-zone transfer time between stations.
Allow user to visualize the line layout.
Allow user to define business rules of queue and logistics of the line layout.
Run simulation of production output and calculate UPH or out-to-out of finished good.

## Slide 4: Example: Route Configuration – Route name and assembly sequence
Start with Route ID or Name
In the route, define the sequence of operations
Lamination
APFA Load
Stacker
Unload
Route: R107

## Slide 5: Example: Route Configuration – Stations and zones
In each operation, define the station name and their zones.
Blue zones are the work zone.
The others are scanning or non-work zones.
Non-work zone has another name, which is a buffer zone.
Each work zone and non-work zone may have the different operation time.
Lamination
APFA Load
Stacker
Unload
Route: R107
ACF Lamination
ZONE 1
ZONE 2
ZONE 3
APFA Load
ZONE 1
ZONE 2
ZONE 3
Auto Stacker
ZONE 1
ZONE 2
ZONE 3

## Slide 6: Example: Route Configuration – Queue stackup
Each station is defined with the number of drive can be received.
For this example, Swage operation has 2 stations (Flip & Swage, and Dual Swage). Dual Swage can work on 2 drives simultaneously, while Flip & Swage can work only one drive.
Once a drive arrived to Swage operation, that drive will be served to Dual Swage. The next drive will be also served into Dual Swage. The 3rd drive then will be served to Flip & Swage.
Stacker
Unload
Route: R107
Auto Stacker
ZONE 1
ZONE 2
ZONE 3
Swage
Flip & Swage
ZONE 1
ZONE 2
ZONE 3
Dual Swage
ZONE 1
ZONE 2
ZONE 3
1
2
1
ALT

## Slide 7: Example: Operation Time & Transfer Time
Each station and zone will be defined with the operation time and transfer time.
Normally transfer time can be defined with one value and apply to all zones. Anyway some zones may have the exceptional value.
ACF Lamination
Z1
Z2
Z3
Define station’s name
Define the number of zones
Define cycle time of each zone
APFA Load
Z1
Z2
Z3
Define transfer time between zones
Define transfer time between stations’ zones

## Slide 8: Example: Run simulation
Start running the simulator will calculate UPH or cycle time of this assembly route.
Simulator can display in both static report and visual operation.
ACF Lamination
Z1
Z2
Z3
APFA Load
Z1
Z2
Z3
Auto Stacker
Z1
Z2
Z3
Flip & Swage
Z1
Z2
Z3
Dual Swage
Z1
Z2
Z3
ALT
Z1
Z2
Z3
ACF Final Bond
Z1
Z2
Z3
Jet Dispenser
Z1
Z2
Z3
UV
Z1
Z2
Z3
BTI
Z1
Z2
Z3
Dual CT
Z1
Z2
Z3
Shipping Comb
Z1
Z2
Z3
Unload
Z1
Z2
Z3

## Slide 9: Example: Run simulation
ACF Lamination
Z1
Z2
Z3
APFA Load
Z1
Z2
Z3
Auto Stacker
Z1
Z2
Z3
Flip & Swage
Z1
Z2
Z3
Dual Swage
Z1
Z2
Z3
ALT
Z1
Z2
Z3
ACF Final Bond
Z1
Z2
Z3
Jet Dispenser
Z1
Z2
Z3
UV
Z1
Z2
Z3
BTI
Z1
Z2
Z3
Dual CT
Z1
Z2
Z3
Shipping Comb
Z1
Z2
Z3
Unload
Z1
Z2
Z3